Lab 3

Exercise#1: Design an 8:1 multiplexer (without in-built blocks) using two 4:1 multiplexers and one 2:1multiplexer (shown in Fig.1) Use both types of multiplexers as sub circuits in the design.

Boolean Expressions	Logic Diagram
output = i7 s0 s1 s2 + i6 ~s0 s1 s2 + i5 s0 ~s1 s2 + i4 ~s0 ~s1 s2 + i3 s0 s1 ~s2 + i2 ~s0 s1 ~s2 + i1 s0 ~s1 ~s2 + i0 ~s0 ~s1 ~s2
Truth Table or Karnaugh (K) Map

Exercise#2: Design a 1:8 de-multiplexer (without in-built blocks) using three 1:4 de-multiplexers. Use 1:4 de-multiplexers as sub circuits in the design

Boolean Expressions	Logic Diagram
Demux 1 x 8
Truth Table or Karnaugh (K) Map

Exercise#3: Design quad to binary (4-to-2) encoder (without in-built blocks) using logic gates. Display all four input digits using seven segment displays and two output binary bits using hex displays available in logisim simulator.

Boolean Expressions	Logic Diagram
o0=i1 + i3 / 01=i2 + i3
Truth Table or Karnaugh (K) Map

Exercise#4: Design 3-to-8 decoder (without in-built blocks) using two 2-to-4 decoders with enable (E) line
shown in Fig. 2. Use 2:4 decoder as sub circuits in the design.
Boolean Expressions	Logic Diagram
3 to 8 decoder
Truth Table or Karnaugh (K) Map